## Slide 1
RoadRank
Final Demo
Driver Behavior FYP
Nasir Ahmad — G00419630
Bachelor of Engineering (Honours) in Software and Electronic Engineering · Atlantic Technological University · 2025/2026
Notes: Hi everyone, I'm Nasir Ahmad. I'll walk you through RoadRank, my final year project. It's an edge-based driver monitoring system that uses computer vision to detect unsafe driving in real time, and turns safer driving into a game through a leaderboard.

## Slide 2
Recap
What RoadRank is
An edge-based driver monitoring system that detects unsafe driving in real time and gamifies safer driving through a leaderboard.
Semester 1 - Research and models
Trained the behaviour classifier (VGGNet, AlexNet, ResNet) and the Siamese facial verification model in Google Colab and Jupyter.
Notes: Quick recap of where we left off. RoadRank is built around two machine learning models. In Semester 1 I trained a behavior model, comparing AlexNet, VGGNet and ResNet on the REVITSONE Kaggle dataset and a Siamese facial-verification network that confirms who's actually behind the wheel. Both models were prototyped in Google Colab or Jupyter Notebook . Today I'll focus on how those models were stitched into a complete system in Semester 2.

## Slide 3
Architecture Diagram
Notes: Here's the full architecture. A Raspberry Pi 5 runs a Flask camera server that owns the camera and both ML models. It talks over HTTP to a Node.js Express API, which handles user accounts and writes to MongoDB Atlas. The Next.js frontend is what the driver actually sees — live feed, dashboard, leaderboard. And in the background, a small sync worker mirrors the Pi's local behavior log into Mongo every ten minutes and recalculates the leaderboard.

## Slide 4
Timeline
Notes: Briefly on the timeline. Semester 1 went on research, dataset preparation and the three CNN architectures, with a working classifier on the Pi for the Christmas demo. Semester 2 was the full-stack web app. The only big addition to the original proposal was the Siamese verification stage — that became necessary once gamified scoring meant scores had to be tied to a verified identity, not just a username.

## Slide 5
Camera Server
State machine
& Threading
1
unverified
Initial state. The first captured frame triggers start_verify, and the machine moves to verifying.
2
verifying
Each frame is preprocessed and compared against the user's stored faces using the Siamese L1 model. On match -> verify_success.
3
verified
Behaviour classification runs on every other frame. A 5-frame agreement buffer debounces noisy predictions before logging.
Why a single-worker, slot-based handoff?
Capture loop overwrites a single pending frame and signals an event. The worker drains it, runs the model, repeats. Stale frames are dropped, threads never accumulate, the Pi stays responsive.
Notes: The camera server is the heart of the project. It's structured as a three-state machine: unverified, verifying, and verified. The first frame triggers verification; once the Siamese model confirms a match, behavior classification kicks in. Behind the scenes there are three cooperating threads — capture, model worker, and Flask. The trick is the handoff: the capture loop overwrites a single pending-frame slot and signals the worker. If inference is slower than capture — which it often is for VGGNet — older frames are dropped instead of queued. That's what keeps the Pi responsive and prevents memory growth.

## Slide 6
Facial Verification
Frame in
Pi Camera Module 3
Preprocess
Resize 100x100
Normalise 0–1
Embedding
Twin tower
4096-d vector
L1 distance
Compare to
stored faces
Match?
>50% agreement
-> verified
Up to 50 reference frames
ffmpeg pulls 1 frame every 0.33s from the user's setup video, capped at 50, into application_data/verification_images/<user>/.
Scoped by expected user
When a username is supplied, the Pi only compares against that user's folder verification falls from seconds to a fraction of a second.
Thresholds
0.5 per-frame and 0.5 aggregate match thresholds tuned for real-world lighting on the Pi camera, not lab conditions.
Notes: Facial verification works like this. A frame from the Pi camera is resized to 100 by 100, normalised, and passed through the twin-tower embedding network into a 4096-dimensional vector. We compute the L1 distance against every reference image in the user's folder, and require more than fifty percent agreement to confirm identity. The reference images come from a short setup video — ffmpeg pulls one frame every third of a second, capped at fifty. Scoping the search to the expected username drops verification time from seconds to a fraction of a second.

## Slide 7
Behaviour
classification
& debouncing
Per-event scoring
Safe
+10
Turn
+5
Other
-2
Talking
-5
Texting
-10
5-frame agreement
An event is only logged when the last 5 predictions all agree, and only if the label is new. Cuts noise drastically: a one-second commitment gate.
Throughput on the Pi 5
~10 fps capture, classification on every other frame (~5 Hz inference) - best-effort alert posted to Express on a background thread so dangerous behaviours surface immediately.
Notes: Once a driver is verified, behaviour classification runs. The scoring is simple: safe driving earns ten points, a turn earns five, talking and texting cost you. The challenge here was noise — the classifier would flicker between adjacent classes frame-to-frame. So I added a five-frame agreement gate: a behaviour only logs when the last five predictions all agree. Effectively, you have to commit to a behaviour for a full second before it counts. The Pi captures at ten frames per second and classifies every other frame, so about five hertz inference.

## Slide 8
Web Stack
Express API - Node.js - Mongoose
POST /register
bcrypt-hashed passwords, 10 salt rounds
POST /facial-setup
multer upload -> ffmpeg fps=3, max 50 frames per user
POST /login
bcrypt.compare; on success the Pi is told via /set-user
POST /api/alerts - GET/DELETE /api/alerts/:user
real-time channel for dangerous-behaviour notifications
GET /api/behavior-log - GET /api/leaderboard
history + global ranking, both queried from the dashboard
Next.js 14 - React - Pages
Live Feed
polls /frame at 10 Hz, /status every 3 s, behaviour pill colour-coded
Behaviour Dashboard
inline SVG score chart, summary cards, paginated event log
Leaderboard
medals for top 3, score-banded colours, current user highlighted
Notifications
5-second poll for fresh alerts, severity-coloured cards, clear-all
Auth - Login / Register / Facial Setup
dual login (password OR face), localStorage-persisted session
Notes: The web stack splits cleanly into two halves. The Express API on the left handles registration with bcrypt-hashed passwords, facial-setup uploads via multer and ffmpeg, login, and the alerts and behaviour-log endpoints that the dashboard consumes. On the right, the Next.js 14 frontend has a Live Feed that polls the camera server, a Behaviour Dashboard with a score chart, a Leaderboard with medals for the top three, and a Notifications page. There are two ways in: password login, or face-based sign-in driven directly by the camera.

## Slide 9
Score sync
& the
leaderboard
Bulk Write
Pi keeps a JSON log on disk, durable across crashes
sync_score.js mirrors entries into Mongo every 10 minutes
Leaderboard ranks recomputed in a single bulkWrite
Real-time alerts channel still fires immediately for the user-facing case
Per-Event syncing
Single point of failure, any Atlas hiccup drops driving data
Constant chatter from the Pi over an unreliable home network
Notes: The leaderboard is kept in sync by a small Node worker that runs every ten minutes. It mirrors the Pi's local JSON log into MongoDB and re-ranks every user in a single bulk write. The trade-off is intentional — per-event syncing would give an instantly-fresh leaderboard, but a network blip would drop driving data. Batching plus the Pi's durable local log means the system tolerates the backend being offline. Real-time alerts still fire immediately for the user-facing case.

## Slide 10
Results & Evaluation
Behaviour classifier - held-out test accuracy
Chart: 
| VGGNet | AlexNet | ResNet
Accuracy % | 95.44 | 94.32 | 33.16
Facial verification - Siamese network
> 0.9
precision @ 0.5 threshold
> 0.9
recall @ 0.5 threshold
- 70/30 train/test split, 50 epochs, batch size 16
- Real-time verify() on the Pi 5 via picamera2 — verified / not verified overlay
User Testing
- User registered a fresh account on the web app.
- Drove a 10-minute session - observed the final score.
- Surfaced UX improvements to the dashboard flow.
Performance Testing
- Prometheus + NetData monitoring the Pi 5.
- 30-minute run: camera server + sync_score.
- Max CPU temperature reached 85 degC - throttling threshold.
- Risk: thermal throttling and possible crash under load.
Unit Tests (Playwright E2E)
- Playwright drives a real headless Chromium against the app.
- 33 tests across home.spec.js, auth.spec.js, leaderboard.spec.js.
- 33 / 33 pass - full suite runs in parallel in under 2 minutes.
- Auto-starts the Next.js dev server; HTML report via show-report.
Notes: Onto evaluation. The behaviour classifier was tested on a held-out set: VGGNet hit ninety-five point four four percent, AlexNet ninety-four point three two, and ResNet only thirty-three percent — likely a flatten-versus-global-average-pooling issue combined with binary cross-entropy on a five-class problem. VGGNet went into production. The Siamese model achieved precision and recall both above 0.9 at the half-threshold. For testing the app, I ran a user-test session, monitored the Pi with Prometheus and NetData — peaked at eighty-five degrees, right at the throttling threshold — I also wrote thirty-three Playwright end-to-end tests. All thirty-three pass, and the full suite runs in under two minutes.

## Slide 11
Challenges
Real-time inference on a Pi
Naively spawning a thread per captured frame led to thread accumulation and growing latency. Fixed with a single worker, a one-slot pending-frame buffer, and an event-driven handoff, stale frames are dropped, the Pi stays under thermal limits.
Noisy frame-by-frame predictions
The classifier flipped between adjacent classes across consecutive frames, producing useless logs. Solved by requiring 5 consecutive predictions to agree before committing an event, gave a clean human-readable behaviour timeline.
Pi - dashboard recovery
Either side could go down independently. The dashboard now shows an offline card with the exact restart command, and the Pi state machine resets cleanly on /reset the system tolerates either component being restarted mid-session.
Notes: Three challenges worth calling out. First, threading on the Pi — naively spawning a thread per frame caused thread accumulation and growing latency. Fixed with the single-worker, slot-based handoff. Second, frame-by-frame noise — solved by the five-frame agreement gate. And third, recovery — either the Pi or the dashboard can go offline independently, so the dashboard now shows an offline card with the exact restart command, and the Pi state machine resets cleanly on /reset.

## Slide 12
Conclusion
Set out to
Build a real-time driver monitoring system that uses computer vision to recognise the driver and classify driving behavior and makes safer driving rewarding through a leaderboard.
Delivered
An end-to-end working product: Pi-based camera server with a state machine, Express API, MongoDB-backed dashboard, dual-mode authentication, real-time alerts, persistent leaderboard.
Learned
How model choices show up in production: debouncing, throttling, scoped verification. What it takes to make an embedded device and a full web stack work together reliably over a flaky network.
Notes: To wrap up. I set out to build a real-time driver monitoring system that recognises the driver, classifies behaviour, and makes safer driving rewarding through a leaderboard. I delivered an end-to-end working product: Pi camera server with a state machine, Express API, MongoDB-backed dashboard, dual-mode authentication, real-time alerts, and a persistent leaderboard. And along the way I learned what it really takes to make embedded ML and a full web stack cooperate reliably over a flaky network.

## Slide 13
Thank you for listening!
Video Demo:
https://youtu.be/GTDBRtyNb0g
GitHub:
https://github.com/Nasir-AhmadZ/Dashboard
https://github.com/Nasir-AhmadZ/FacialVerificationML
https://github.com/Nasir-AhmadZ/Driver-Analysis-ML-Model
Questions?
Supervisor: Ben Kinsella
Atlantic Technological University